SECTION 11 66 53.13

PROTECTIVE GYMNASIUM FLOOR COVERS

PART 1 - GENERAL

1.1	SUMMARY

***** Edit list as required for specific project. *****

A.	Section includes:

- Protective gymnasium floor covers

- Gym Floor Cover Handling System/Storage Cart

- Accessories:

  - Power Winder

  - Sweeper Strip

  - Handheld Tape Dispenser

  - Walk Behind Tape Dispenser

  - Seaming Tape

  - Storage Cart Cover

D.	Related sections:

***** List other specification sections dealing with work directly related to this section such as the following. *****

1.2	SUBMITTALS

A.	Submit in accordance with Section 01 33 00 [01330] - Submittal Procedures:

1.	List of proposed products and product data.

2.	Shop drawings showing layout, elevations, dimensions, fabrication details, method of attachment, and electrical wiring diagrams as appropriate.

4.	Samples of fabric.

5.	Manufacturer's assembly/installation and maintenance instructions.

1.3	QUALITY ASSURANCE

A.	Source limitation: All components including cover, handling system and accessories shall be products of a single manufacturer.

1.4	DELIVERY, STORAGE, AND HANDLING

*****In order to reduce potential damage to floor cover and related equipment, it is desirable to deliver after gymnasium flooring and other interior construction is essentially complete. *****

A.	Do not deliver floor cover and related equipment until building is enclosed and, other construction within gymnasium is substantially complete.

PARTS 2 - PRODUCTS

2.1	ACCEPTABLE MANUFACTURERS

A.	Draper, Inc., 411 South Pearl Street, Spiceland, Indiana 47385-0425; 765-987-7999.

B.	Manufacturers of equivalent products submitted and approved in accordance with Section 01630 - Product Substitution Procedures.

2.2	PROTECTIVE GYMNASIUM FLOOR COVER

A.	Type: Protective Gymnasium Floor Covers to be Floor Protection Cover as manufactured by Draper, Inc.

B.	Material Properties: Protective Gymnasium Floor Cover to meet or exceed the following properties:

- Fabric Weight: Average of 22 ounces per square yard per ASTM D37776.

- Fabric Construction: Vinyl laminated to front and back surface of 9 x 9, 1,000 denier polyester scrim.

- Colors: Fabrics are duplex fabrics with different colors on each surface. Color combinations are Beige/Blue or Grey/Red.

- Finish: Fabric to feature a micro-taffeta finish to provide excellent slip resistance.

- Tensile Strength: 216 Lbs. x 231 Lbs. per ASTMD5035.

- Tear Strength: 87 lbs. x 83 Lbs. per ASTM D226.

- Flame Retardant: Pass NFPA,701 or equivalent UL-214.

- Treatments: Fabric to be treated to be resistant to water, rot, mildew, fungus, odor, and fading from ultraviolet light.

C. 	Configuration: Sufficient material to be supplied to cover [entire gymnasium floor] [section of gym floor measuring _____ x ______]. Cover is supplied in 10’ wide sections made from 10’ wide rolled goods. Vertical seams along the length of the floor cover are not acceptable. Floor cover to be supplied in the required length with a maximum length of 120’ per section. Fabric is laid on gymnasium floor with approximately 2” overlap between sections.

2.3	PROTECTIVE GYMNASIUM FLOOR COVER HANDLING SYSTEM

***** Include the following paragraphs for to storage cart(s) for gym floor protection cover *****

*****************************************************************************

A.	Type: Floor protection storage/transportation cart is to be model no. [502499] [502500], [Six] [Eight]-Roll Floor Protection Cover Cart by Draper, Inc. Spiceland, IN.

B	Construction: Floor Protection Cover Cart is constructed of 1½" x 14-gauge square tubing and ¼" thick steel plate and finished with an attractive gloss black powder coat. Cart features six 6" non-marking casters to distribute weight of cart and covers across a larger floor surface area. Cart has folding outriggers that are locked in the down position during use and dual floor locks to hold the cart in place. Overall dimensions of cart are 148-3/8" (l) x 30" (w) x 60-5/8" (h). Width allows for cart to go through a standard door and outriggers that provide a total width of 52¾" when in the down position, remove any possibility of tip-ping. Fabric rolls on zinc plated 2-3/8" OD roller tubes that are captured in four-roller, bearing plates to insure easy operation. Roller tubes include through pins at each end to accept hand cranks at each end for easy rolling of Floor Protection Cover. Cover attaches quickly and easily to roller tubes with flexible plastic clips and is secured in the rolled position with hook and loop straps. Each cart is supplied with two hand cranks plus four flexible plastic clips and one hook and loop strap for each roller tube. Cart base includes shelves at each end and in the middle for storage of crank handles, clips, straps and other accessories.

2.4	PROTECTIVE GYMASIUM FLOOR COVER SYSTEM ACCESSORIES

***** Include in combination of the following paragraphs to include accessories for gym floor protection cover system *****

*****************************************************************************

- Provide Draper Model 502550–Power Winder. Powerful handheld portable drive unit that features a 115-volt, 1200-watt motor to produce over 250 ft-lbs. of torque. Drive unit is reversible and includes a heavy-duty snap in drive adaptor to make rolling Floor Protection Cover quick and easy.

- Provide Draper Model 502520-Sweeper Strip. Strip of soft 2½" long bristles to clean Floor Protection Cover as it is rolled on to cart. Sweeper Strip brackets bolt on to cart and strip is moved side-to-side as cover is rolled onto tubes.

***** Include only one style of tape dispenser by picking one of the next two paragraphs *****

*****************************************************************************

- Provide Draper Model 502531–Handheld Tape Dispenser. Dispenser has a heavy-duty steel frame and comfortable plastic pistol grip. Dispenser holds one 3" wide roll of seaming tape and has a double side cutting blade.

- Provide Draper Model 502532–Walk-Behind Tape Dispenser. Dispenser has a tubular construction with three wheels for stability during use. Front wheel is 7" wide and presses tape to surface while user pushes.

*****************************************************************************

- Provide Draper Model 502533–Floor Protection Cover Seaming Tape. Three-inch wide clear nylon tape to secure edges and seams of Floor Protection Cover to reduce trip hazards and make more waterproof. Seaming tape is sold by the carton of sixteen 36-yard rolls. Tape removes easily and does not leave adhesive residue.

- Provide Draper Model 5025XX-Floor Protection Storage Cart Cover. Cart cover is constructed of 14 oz. leather grain embossed vinyl fabric sewn to allow cover to completely cover cart. Cover keeps cart and cover material clean and prevents people form climbing on and damaging floor protection system during storage. Cover to be [white] [marine blue] [red] [beige] [orange] [yellow] [grey] [maroon] [dark/royal blue] [black] [purple] [forest green] [kelly green] [navy blue] as chosen by architect or owner.

PART 3 - EXECUTION

3.1	PREPARATION

*****Typically, Protective Gymnasium Floor Covers are provided, assembled and installed by local manufactures representative who will address items in this section*****

- Coordinate configuration and size of protective gymnasium floor cover to ensure it is properly sized to cover desired area of floor. Field verify dimensions prior to fabrication.

- Coordinate delivery of protective gymnasium floor cover so that it arrives after building is enclosed and, other construction within gymnasium is substantially complete.

- If delivered prior other construction within gymnasium being substantially complete, protective gymnasium floor cover, cover handling system and accessories should be protected from damage during construction. Do not use gymnasium floor cover, handling system or accessories to protect gymnasium floors during construction.

3.2	INSTALLATION/ASSEMBLY

A.	Install and assemble in accordance with manufacturer's written instructions and shop drawings.

3.3	TESTING AND DEMONSTRATION

A.	Demonstrate to Owner's designated representative, complete use and required maintenance.

END OF SECTION