SECTION 11 66 23. 56 [11480]

WRESTLING MAT STORAGE

PART 1 - GENERAL

1.1	SUMMARY

A.	Section includes:

- Wrestling Mat Hoist.

B.	Related sections:

- Section [____] - [__________]: Structural steel framing to support Mat Hoist.

- Section [____] - [__________]: Electrical supply, conduit, and wiring for Mat Hoist.

1.2 SUBMITTALS

A.	Submit in accordance with Section 01 33 00 [01330]- Submittal Procedures:

- List of proposed products and product data.

- Shop drawings showing layout, elevations, dimensions, fabrication details, method of attachment, and electrical wiring diagrams.

- Manufacturer's installation and maintenance instructions.

1.3	QUALITY ASSURANCE

A.	Source limitation: All components including suspension system, frame assembly, controls for mat lifter, shall be products of a single manufacturer.

1.4	DELIVERY, STORAGE, AND HANDLING

A.	Do not deliver equipment until building is enclosed and other construction within gymnasium is substantially complete.

PART 2 - PRODUCTS

2.1	ACCEPTABLE MANUFACTURERS

A.	Draper, Inc., 411 South Pearl Street, Spiceland, Indiana 47385-0425; 765-987-7999.

- Manufacturers of equivalent products submitted and approved in accordance with Section 01 23 00 [01360] - Product Substitution Procedures.

2.2	 WRESTLING MAT HOIST (ONE REQUIRED)

A.	Type: Model No. 502060 Single Mat Lifter

B.	Construction: Mat Lifter construction shall consist of a [20 foot] [6.1 meters] I-beam frame, with all drive and lifting mechanism enclosed in a sheet metal housing. Unit shall be a three cable system to assure balanced operation. Cables shall be attached to the I-beam frame and attach to the load bar, which shall be connected to fabric slings. Standard lifter, load bar, and sling shall be capable of supporting one standard [45 x 45 feet] [13.7 x 13.7 meters] wrestling mat (weighing approximately [1 lb. per square foot] [4.882 kg per square meter]). Mats may be one piece or in sections placed end-to-end.

Each unit shall consist of a highly efficient hollow bored helical gear direct drive ([1.5 inch] [38 mm] diameter) solid key shaft to an instantly reversing 1 HP motor, operating with 208/230/460 volts in 3-phase, including a [7.4 lb.] [3.4 kg] fast action brake. Lifting and lowering speed shall be approximately [10 feet] [3.048 meters] per minute. System shall have a custom integrated motion alarm which automatically sounds when system is in motion for safety.

Lifting drums shall be [4 inch] [10.1 cm] diameter directly coupled to a [1.5 inch x 20 feet] [38 mm x 6.1 meters] solid keyed shaft. Three steel lift cables shall be [5/16 inch x 35 foot] [7.8 mm x 10.668 meters] 7 x 19 aircraft cable. Cables shall be rated at [1960 lbs.] [889 kg] each at a 5-to-1 safety factor. System shall include an emergency lowering manual override brake, in case of power outage.

40 foot [12.19 meters] Load bar shall be connected to [22 ounce] [.6237 kg] vinyl/polyester super sling able to accommodate up to a [40 inches] [101.6 cm] diameter mat, with heavy duty straps and fasteners. Standard sling color is black; other colors are available by special request. For safety purposes, sling capacity shall govern the lift capacity of the system. Motors, drive assembly, and all control mechanisms shall be encased in a fire proof safety cover. Warranty shall be 5 years.

Movement control shall be prewired with a furnished electrical key switch wired to an intrinsically safe 24 volt power system with automatic off return and raise/lower legend plate.

Wiring and conduit from hoist to key switch and electrical hook-up of unit by others.

Approximate unit weight shall be [1,750 lb.] [794 kg] (not including mat).

***** As an option, a traveling kit can be provided for Mat Lifters. Include the following paragraphs if traveling kit is required.

- Mat Lifter Travel Kit shall be driven by a .50 HP motor operating with 208/230/460 volts in 3-phase attached to a 60:1 ratio gear box with non-pneumatic wheel (s).

***** Choose appropriate traveling kit for the desired method of travel.

- End First travel kit for unit shall have two [1-ton] [907 kg] machined trolleys with festooning power cables. Motors, drive assembly, and all control mechanisms shall be encased in a fireproof safety cover.

- Sideways travel kit shall have four [½-ton] [454 kg] machined trolleys with festooning power cables. Motors, drive assembly, and all control mechanisms shall be encased in a fireproof safety cover.

## Electrical Contractor Shall Provide and Install:

All conduits complete with wire from power source to control enclosure, from control enclosure to unit.

PART 3 - EXECUTION

3.1	PREPARATION

A.	Coordinate support of mat lifter with roof or wall structure to ensure proper distribution of loads and adequacy of attachment points. Ensure that building structure has been designed for loads of specific mat lifter to be provided. Provide additional structural framing members as required in accordance with Section [_____] - [__________].

B.	Coordinate configuration, size, and installation of mat lifter with height, slope, and type of building structure and lighting fixtures, mechanical equipment, ductwork, fire-suppression system, bleachers, athletic equipment, and other potential obstructions.

- Field verify dimensions prior to fabrication.

- Coordinate electrical requirements for motorized operating mechanism to ensure proper power source, conduit, wiring, and boxes for keyed switches. Prior to installation, verify type and location of power supply. See “Electrical Contractor Shall Provide and Install”

- Painting: Mat Lifter and parts shall be factory painted neutral gray enamel paint.

- For installations made after wood gymnasium flooring is installed, provide protection and exercise care not to damage flooring.

- Coordinate unloading and transport of mat lifter into facility insuring there is ample room to navigate large equipment into are where it is to be installed.

3.2	INSTALLATION

A.	Install in accordance with manufacturer's written instructions and shop drawings.

B.	Install even, plumb and level.

C.	Install control switch such that operator has view of complete mat lifter during lowering and raising.

D.	Adjust limit switches to ensure accurate position in both stored and lowered positions.

3.3	TESTING AND DEMONSTRATION

A.	Operate mat lifter to ensure proper lifting and lowering. Adjust as required to ensure smooth operation and accurate positioning.

B.	Demonstrate to Owner's designated representatives complete operation and required maintenance.

END OF SECTION